vignesh@vignesh-HP-Pavilion-Laptop-15-cc1xx:~$ rosrun camera_calibration cameracalibrator.py --size 5x5 --square 0.021 image:=/usb_cam/image_raw camera:=/usb_cam
Waiting for service /usb_cam/set_camera_info ...
OK
*** Added sample 1, p_x = 0.331, p_y = 0.300, p_size = 0.654, skew = 0.113
*** Added sample 2, p_x = 0.142, p_y = 0.497, p_size = 0.655, skew = 0.106
*** Added sample 3, p_x = 0.263, p_y = 0.482, p_size = 0.627, skew = 0.168
*** Added sample 4, p_x = 0.148, p_y = 0.344, p_size = 0.616, skew = 0.126
*** Added sample 5, p_x = 0.369, p_y = 0.421, p_size = 0.547, skew = 0.167
*** Added sample 6, p_x = 0.250, p_y = 0.219, p_size = 0.636, skew = 0.057
*** Added sample 7, p_x = 0.197, p_y = 0.473, p_size = 0.473, skew = 0.095
*** Added sample 8, p_x = 0.154, p_y = 0.796, p_size = 0.558, skew = 0.021
*** Added sample 9, p_x = 0.182, p_y = 0.535, p_size = 0.603, skew = 0.017
*** Added sample 10, p_x = 0.620, p_y = 0.388, p_size = 0.514, skew = 0.398
*** Added sample 11, p_x = 0.644, p_y = 0.227, p_size = 0.552, skew = 0.347
*** Added sample 12, p_x = 0.376, p_y = 0.241, p_size = 0.529, skew = 0.094
*** Added sample 13, p_x = 0.573, p_y = 0.276, p_size = 0.520, skew = 0.102
*** Added sample 14, p_x = 0.385, p_y = 0.625, p_size = 0.567, skew = 0.053
*** Added sample 15, p_x = 0.609, p_y = 0.555, p_size = 0.567, skew = 0.053
*** Added sample 16, p_x = 0.381, p_y = 0.369, p_size = 0.461, skew = 0.031
*** Added sample 17, p_x = 0.581, p_y = 0.372, p_size = 0.401, skew = 0.046
*** Added sample 18, p_x = 0.554, p_y = 0.247, p_size = 0.427, skew = 0.013
*** Added sample 19, p_x = 0.319, p_y = 0.638, p_size = 0.198, skew = 0.066
*** Added sample 20, p_x = 0.241, p_y = 0.471, p_size = 0.264, skew = 0.142
*** Added sample 21, p_x = 0.180, p_y = 0.594, p_size = 0.247, skew = 0.081
*** Added sample 22, p_x = 0.241, p_y = 0.529, p_size = 0.213, skew = 0.236
*** Added sample 23, p_x = 0.300, p_y = 0.546, p_size = 0.239, skew = 0.411
*** Added sample 24, p_x = 0.599, p_y = 0.414, p_size = 0.233, skew = 0.381
*** Added sample 25, p_x = 0.810, p_y = 0.491, p_size = 0.239, skew = 0.341
*** Added sample 26, p_x = 0.554, p_y = 0.644, p_size = 0.177, skew = 0.157
*** Added sample 27, p_x = 0.445, p_y = 0.686, p_size = 0.181, skew = 0.017
*** Added sample 28, p_x = 0.363, p_y = 0.597, p_size = 0.164, skew = 0.349
*** Added sample 29, p_x = 0.704, p_y = 0.507, p_size = 0.230, skew = 0.147
*** Added sample 30, p_x = 0.531, p_y = 0.402, p_size = 0.209, skew = 0.148
*** Added sample 31, p_x = 0.619, p_y = 0.554, p_size = 0.230, skew = 0.072
*** Added sample 32, p_x = 0.631, p_y = 0.649, p_size = 0.227, skew = 0.239
*** Added sample 33, p_x = 0.608, p_y = 0.604, p_size = 0.211, skew = 0.373
*** Added sample 34, p_x = 0.630, p_y = 0.463, p_size = 0.232, skew = 0.230
*** Added sample 35, p_x = 0.561, p_y = 0.347, p_size = 0.228, skew = 0.044
*** Added sample 36, p_x = 0.343, p_y = 0.131, p_size = 0.252, skew = 0.028
*** Added sample 37, p_x = 0.524, p_y = 0.322, p_size = 0.223, skew = 0.307
*** Added sample 38, p_x = 0.714, p_y = 0.350, p_size = 0.223, skew = 0.453
*** Added sample 39, p_x = 0.685, p_y = 0.272, p_size = 0.239, skew = 0.359
*** Added sample 40, p_x = 0.717, p_y = 0.369, p_size = 0.229, skew = 0.265
*** Added sample 41, p_x = 0.734, p_y = 0.375, p_size = 0.230, skew = 0.075
**** Calibrating ****
mono pinhole calibration...
D = [-0.015314286843921835, 0.010552927420486071, 0.0013508497744202544, 0.0009702042359838577, 0.0]
K = [486.69571360634427, 0.0, 332.0468666469895, 0.0, 484.1177796393465, 281.25052225084767, 0.0, 0.0, 1.0]
R = [1.0, 0.0, 0.0, 0.0, 1.0, 0.0, 0.0, 0.0, 1.0]
P = [484.5396316849037, 0.0, 332.76715280220463, 0.0, 0.0, 482.2241681769743, 281.9260191397327, 0.0, 0.0, 0.0, 1.0, 0.0]
None
# oST version 5.0 parameters

[image]

width
640

height
480

[narrow_stereo]

camera matrix
486.695714 0.000000 332.046867
0.000000 484.117780 281.250522
0.000000 0.000000 1.000000

distortion
-0.015314 0.010553 0.001351 0.000970 0.000000

rectification
1.000000 0.000000 0.000000
0.000000 1.000000 0.000000
0.000000 0.000000 1.000000

projection
484.539632 0.000000 332.767153 0.000000
0.000000 482.224168 281.926019 0.000000
0.000000 0.000000 1.000000 0.000000

('Wrote calibration data to', '/tmp/calibrationdata.tar.gz')
D = [-0.015314286843921835, 0.010552927420486071, 0.0013508497744202544, 0.0009702042359838577, 0.0]
K = [486.69571360634427, 0.0, 332.0468666469895, 0.0, 484.1177796393465, 281.25052225084767, 0.0, 0.0, 1.0]
R = [1.0, 0.0, 0.0, 0.0, 1.0, 0.0, 0.0, 0.0, 1.0]
P = [484.5396316849037, 0.0, 332.76715280220463, 0.0, 0.0, 482.2241681769743, 281.9260191397327, 0.0, 0.0, 0.0, 1.0, 0.0]
# oST version 5.0 parameters

[image]

width
640

height
480

[narrow_stereo]

camera matrix
486.695714 0.000000 332.046867
0.000000 484.117780 281.250522
0.000000 0.000000 1.000000

distortion
-0.015314 0.010553 0.001351 0.000970 0.000000

rectification
1.000000 0.000000 0.000000
0.000000 1.000000 0.000000
0.000000 0.000000 1.000000

projection
484.539632 0.000000 332.767153 0.000000
0.000000 482.224168 281.926019 0.000000
0.000000 0.000000 1.000000 0.000000

QObject::~QObject: Timers cannot be stopped from another thread
vignesh@vignesh-HP-Pavilion-Laptop-15-cc1xx:~$

camera matrix for the logi camera

vignesh@vignesh-HP-Pavilion-Laptop-15-cc1xx:~$ rosrun camera_calibration cameracalibrator.py --size 5x5 --square 0.0201 image:=/usb_cam/image_raw camera:=/usb_cam
Waiting for service /usb_cam/set_camera_info ...
OK
*** Added sample 1, p_x = 0.063, p_y = 0.570, p_size = 0.290, skew = 0.024
*** Added sample 2, p_x = 0.205, p_y = 0.630, p_size = 0.285, skew = 0.005
*** Added sample 3, p_x = 0.071, p_y = 0.403, p_size = 0.287, skew = 0.052
*** Added sample 4, p_x = 0.239, p_y = 0.420, p_size = 0.278, skew = 0.018
*** Added sample 5, p_x = 0.129, p_y = 0.121, p_size = 0.302, skew = 0.108
*** Added sample 6, p_x = 0.087, p_y = 0.544, p_size = 0.284, skew = 0.295
*** Added sample 7, p_x = 0.389, p_y = 0.819, p_size = 0.271, skew = 0.008
*** Added sample 8, p_x = 0.548, p_y = 0.460, p_size = 0.250, skew = 0.006
*** Added sample 9, p_x = 0.643, p_y = 0.556, p_size = 0.266, skew = 0.075
*** Added sample 10, p_x = 0.388, p_y = 0.556, p_size = 0.253, skew = 0.012
*** Added sample 11, p_x = 0.407, p_y = 0.405, p_size = 0.266, skew = 0.077
*** Added sample 12, p_x = 0.517, p_y = 0.453, p_size = 0.276, skew = 0.165
*** Added sample 13, p_x = 0.715, p_y = 0.459, p_size = 0.276, skew = 0.052
*** Added sample 14, p_x = 0.894, p_y = 0.423, p_size = 0.283, skew = 0.041
*** Added sample 15, p_x = 0.901, p_y = 0.585, p_size = 0.305, skew = 0.127
*** Added sample 16, p_x = 0.891, p_y = 0.443, p_size = 0.300, skew = 0.209
*** Added sample 17, p_x = 0.824, p_y = 0.232, p_size = 0.307, skew = 0.454
*** Added sample 18, p_x = 0.739, p_y = 0.316, p_size = 0.291, skew = 0.380
*** Added sample 19, p_x = 0.694, p_y = 0.467, p_size = 0.298, skew = 0.238
*** Added sample 20, p_x = 0.655, p_y = 0.380, p_size = 0.308, skew = 0.088
*** Added sample 21, p_x = 0.527, p_y = 0.205, p_size = 0.319, skew = 0.094
*** Added sample 22, p_x = 0.497, p_y = 0.418, p_size = 0.286, skew = 0.307
*** Added sample 23, p_x = 0.393, p_y = 0.889, p_size = 0.351, skew = 0.082
*** Added sample 24, p_x = 0.084, p_y = 0.235, p_size = 0.334, skew = 0.492
*** Added sample 25, p_x = 0.094, p_y = 0.123, p_size = 0.325, skew = 0.562
*** Added sample 26, p_x = 0.111, p_y = 0.530, p_size = 0.348, skew = 0.479
*** Added sample 27, p_x = 0.127, p_y = 0.493, p_size = 0.521, skew = 0.176
*** Added sample 28, p_x = 0.115, p_y = 0.222, p_size = 0.534, skew = 0.122
*** Added sample 29, p_x = 0.241, p_y = 0.435, p_size = 0.475, skew = 0.127
*** Added sample 30, p_x = 0.267, p_y = 0.756, p_size = 0.478, skew = 0.122
*** Added sample 31, p_x = 0.367, p_y = 0.486, p_size = 0.448, skew = 0.095
*** Added sample 32, p_x = 0.523, p_y = 0.574, p_size = 0.438, skew = 0.216
*** Added sample 33, p_x = 0.883, p_y = 0.762, p_size = 0.439, skew = 0.092
*** Added sample 34, p_x = 0.916, p_y = 0.657, p_size = 0.421, skew = 0.253
*** Added sample 35, p_x = 0.738, p_y = 0.656, p_size = 0.436, skew = 0.245
**** Calibrating ****
mono pinhole calibration...
D = [0.03018090750318232, 0.14677562590767443, 0.0003970510118694169, -0.012457738865256952, 0.0]
K = [794.5324428989027, 0.0, 287.1463077155482, 0.0, 793.915658900354, 240.33004146867466, 0.0, 0.0, 1.0]
R = [1.0, 0.0, 0.0, 0.0, 1.0, 0.0, 0.0, 0.0, 1.0]
P = [805.5326493954259, 0.0, 282.85666708622, 0.0, 0.0, 811.0700897811595, 240.43566129597062, 0.0, 0.0, 0.0, 1.0, 0.0]
None
# oST version 5.0 parameters

[image]

width
640

height
480

[narrow_stereo]

camera matrix
794.532443 0.000000 287.146308
0.000000 793.915659 240.330041
0.000000 0.000000 1.000000

distortion
0.030181 0.146776 0.000397 -0.012458 0.000000

rectification
1.000000 0.000000 0.000000
0.000000 1.000000 0.000000
0.000000 0.000000 1.000000

projection
805.532649 0.000000 282.856667 0.000000
0.000000 811.070090 240.435661 0.000000
0.000000 0.000000 1.000000 0.000000

('Wrote calibration data to', '/tmp/calibrationdata.tar.gz')
D = [0.03018090750318232, 0.14677562590767443, 0.0003970510118694169, -0.012457738865256952, 0.0]
K = [794.5324428989027, 0.0, 287.1463077155482, 0.0, 793.915658900354, 240.33004146867466, 0.0, 0.0, 1.0]
R = [1.0, 0.0, 0.0, 0.0, 1.0, 0.0, 0.0, 0.0, 1.0]
P = [805.5326493954259, 0.0, 282.85666708622, 0.0, 0.0, 811.0700897811595, 240.43566129597062, 0.0, 0.0, 0.0, 1.0, 0.0]
# oST version 5.0 parameters

[image]

width
640

height
480

[narrow_stereo]

camera matrix
794.532443 0.000000 287.146308
0.000000 793.915659 240.330041
0.000000 0.000000 1.000000

distortion
0.030181 0.146776 0.000397 -0.012458 0.000000

rectification
1.000000 0.000000 0.000000
0.000000 1.000000 0.000000
0.000000 0.000000 1.000000

projection
805.532649 0.000000 282.856667 0.000000
0.000000 811.070090 240.435661 0.000000
0.000000 0.000000 1.000000 0.000000

QObject::~QObject: Timers cannot be stopped from another thread